## Slide 1
ELM–PFLOTRAN weak coupling (per column)
sequential / offline exchange — each model keeps its own solver, timestep and code base; files are the interface
NLDAS-2 met forcing — 0.125° / 12 km (rain·snow·T·wind·humidity·radiation)
ELM — E3SM Land Model (surface & root zone, 0–3.8 m + bucket aquifer)
• snow & canopy · evapotranspiration · runoff partitioning
• per-column SSURGO soil surface data · NLDAS forcing
• warm-started at the Fan water table (finidat)
→ outputs: daily infiltration QINFL · runoff · restart states
① one-way — LIVE
daily QINFL → top
Neumann flux BC
② feedback — PLANNED
water-table depth / capillary
rise → ELM bottom BC;
iterate until WTD converges
PFLOTRAN — Richards vadose zone (variably saturated, 1-D to ~50 m)
• van Genuchten curves from the same SSURGO horizons
• hydrostatic IC + bottom pinned at the Fan water table
• ~1 s per column, serial — no batch queue
→ outputs: recharge AT the water table · lag & attenuation · saturation profiles
water table — Fan 2013 equilibrium prior (ParFlow-CONUS2 upgrade wired)
0 m
3.8 m
~50 m (cap)
why WEAK coupling
• no source-code intrusion — either model can be swapped or upgraded independently
• each model runs at its own resolution & timestep
• exchange = per-column files (flux series, restart states)
evidence (Naches, 18/20 columns):
• infiltration→water-table lag: 0 d (WTD<1 m) → 7–104 d (5–35 m)
• vadose zone = low-pass filter; cutoff set by WTD
legend:
— solid blue: implemented (one-way)
- - dashed orange: planned (two-way)
shared per-column context (columns.json): same site, same SSURGO soil profile, same Fan-WTD prior — the models see one consistent world

## Slide 2
Multi-agent framework — current architecture
Data Layer
MCP servers (agent tools):
terrain 3DEP/WBD · geology SSURGO · usgs_water wells+gauges · snotel SWE · weather · fan_wtd
Bulk products (build time):
NLDAS-2 forcing 12 km (default) · Fan WTD warm-start prior · ParFlow-CONUS2 (wired)
Reception Agent
agentic LLM tool-user — drives MCP itself
intent + archetype routing · evidence gathering · interactive clarification · multi-turn context
USER
question
clarifications
agentic tool loop
Planner Agent
capability-aware LLM designer
• strategy: N, strata, validation targets
• feasibility verdict vs execution limits
• requires_capabilities backlog
• altitude only — NO coordinates
• internal validation loop
Experiment Manager
deterministic pipeline — strategy in, results out
ELM per-column · PFLOTRAN 1-D — same interface
1. materialize sampling (DEM·soil·WTD)
2. build & configure (forcing · warm start)
3. pre-flight guards
4. execute (concurrent · cost confirm)
5. collect (history · restarts)
Analyzer
numbers → validation → LLM interpretation
a. water budgets · driver×response matrix · honesty flags
b. observation validation: wells · gauges (NSE/KGE) · SNOTEL
c. LLM interpreter (Answer/Why/Trust/Next)
→ auto-generated storyline deck
framed brief JSON
strategy
results
analyze existing exp.
final report + deck
DEM·soil·WTD·forcing (bulk)
observations for validation
anti-hallucination boundary — the LLM plans strategy; every coordinate & config comes from data
chained experiments: a run's outputs (ELM infiltration, restarts) feed the next build — warm starts · ELM→PFLOTRAN coupling